Great Plains 706

TO USERS OF THE NEW CASTLE CONSERVATION DISTRICT NO-TILL DRILL

Plants 7' wide with 7.5" rows, drawbar hitch, 55HP with hydraulics, 1+ ton and supply your own hitchpin

No Fertilizer to be put in seed hoppers

Calibration of the drill according to the "Operators Manual" found in the toolbox gives the best available estimate for the specific seeding rates.   The New Castle Conservation District accepts no responsibility for the accuracy of the setting.

LUBRICATE THE DRILL ACCORDING TO OPERATORS MANUAL-PER USE

Before using the drill:

(	Engage each lock out hub, remove both cylinder locks.

- Check for any loose or broken parts.  Check Tires.

(	Check Seed Tubes for spider webs (especially small seed tubes).

(	Raise the hitch stand.

(	Install the safety chain.

(	Set the acreage meter to "O".

(	Operate at a ground speed of 4-6 mph.

After using the drill:

(	Lock up the hydraulic cylinders.

Disengage drive lock out hubs on both wheels.

(	Clean out seed from all hoppers and tubes.  Vacuum or blow out the hoppers, clean out feed cups by dropping latch all the way down, and shake out the tubes.  If you used the small seed hopper, remove the drive chain and place in tool box.  There is a $50 hourly charge for not cleaning seed out of the drill.

(	Read the acreage meter.

Transport:

- Disengage drive lockout hubs before transporting.  Please refer to          pages 21-22 for further transporting instructions.

(	Call Elizabeth Hook at 832-3100 extension 8970 to report completion and acres.  The next farmer will pick it up from you. The District will send you a bill.

Repairs Needed:

(	Call Elizabeth Hook at 832-3100 extension 8970.

(	If she is not available and parts or repairs are needed call Atlantic Tractor at 410-275-2195 in Cecilton, MD.

IMPORTANT: NEVER backup with openers in the ground.  Seed chart is located in drill.